## Slide 1
Radar Enabled Camera Trap
Presented by Group 8
Designed For Behavioral Monitoring Of Fork-Tailed Drongos

## Slide 2
Introduction and Problem Statement
Ben Murphy is studying Southern Yellow-Billed Hornbills and Fork-tailed Drongos in the Kalahari desert.
He is researching the decline in breeding success of the Hornbills due to rising temperatures while the breeding success of the Drongos remains stable.
He needs a method to consistently capture footage of the Drongos for behavioural analysis, as his current techniques lack reliability.

## Slide 3
Proposed Solution
Use multiple sensors to ensure reliability: PIR, mmWave, Acoustic, Weight.
Cost effective and reusable system.
Solar power and battery system for indefinite operation.
Wireless data retrieval to avoid climbing trees.

## Slide 4
Powering The Camera Trap
Low-cost
Environmentally friendly
Battery powered
Ability to use solar panel input for power

## Slide 5
Power Management
Features:
Protection circuitry
Priority switching
Under-voltage
Over-voltage
Long battery life

## Slide 6
Future Enhancements
Optimise battery charging
Printed circuit board (PCB) transition
Protective system enclosure
Address voltage drop issue

## Slide 7
Sensing and System Triggering
Reduction in missed triggers
Improvement in low-light conditions
Radar and PIR Dual Sensing System

## Slide 8
System Features and Performance
Adjustable Sensitivity
Multi-Trigger Handling
False Trigger Filtering
<50ms Trigger Event

## Slide 9
Future Enhancement
In the field testing needed
Stationery object detection
Reduce radar power consumption

## Slide 10
Camera and Footage Capture
Camera is a crucial decision of the final product
Needs to be cost effective, power efficient and have good quality
ESP32-Cam with OV5640

## Slide 11
ESP32 and OV5640
Low cost of R300
Starts recoding in < 1 second
High quality 2560 x 1920p
Records at 12fps 480p
Adjustable focal point
Poor performance in low light

## Slide 12
Close (30 cm)
Medium (1m)
Far (3m)
Low light

## Slide 13
Optimizations and Enhancements
Raspberry Pi paired with the 12MP Pi Camera Module V3 with Motorized PDAF.
Machine learning algorithm to estimate the presence of a bird

## Slide 14
Front End System
Data Storage – Store large video files
Data Processing – Creating Usable Statistics
Ease of access to data – download files wirelessly
Raspberry Pi local host web server ticks these boxes

## Slide 15
Wireless Data Storage and Processing
Files are wirelessly transferred from the camera system to the storage system.
These files include pictures, videos and text files containing data
Data files are processed to give useful statistics, using a combination of scripts.

## Slide 16
Website and Data Downloading
Connects via a Wi-Fi hotspot
Allows system interaction
View and Download picture and video files wirelessly (No more climbing trees)
View Graphs with useful statistics
View system analytics (Remaining storage, etc)

## Slide 17
Conclusion
Successfully proved multiple concepts:
  Multi sensor triggering
  Footage capture and storage
  Solar power and power management
  Wireless user-friendly interface
Further refinements and enhancements outlined for next iteration.
Camera trap housing needs to be developed.